## Slide 1: SMART INDIA HACKATHON 2026
Problem Statement ID –260168
Problem Statement Title- AI-ML based Intelligent Dead Reckoning system for seamless navigation
Theme- Smart Vehicles
PS Category- Software
Team ID- 132834
Team Name (Registered on portal)- @enigm@

## Slide 2: Edge-Native Virtual Odometer & Zero-Drift GNSS Fusion Engine
@Enigm
@
NaviCore AI
2
@SIH Idea submission- Template
@Enigm
@
Auto-Calibration (LPF + PCA)
AI Odometer · NHC · ZUPT
6-DOF IMU @ 100 H
HMM Map-Matching (OSM)
ESKF GNSS + INS Fusion
Smooth 10 Hz Navigation UI
PROBLEM EXISTING
GNSS Blackouts : Tunnels, urban canyons & parking lots kill satellite signal.
No OBD-II Link : Most Indian 2-wheelers & budget cars rely only on a phone, with no wheel-speed sensor.
Double-Integration Drift : Cheap MEMS IMU bias grows quadratically, drifting hundreds of metres in seconds.
Environmental Noise : Potholes, braking & idling vibration corrupt standard filters.
PROPOSED SOLUTION
A. AI Virtual Odometer : 1D-CNN/TCN turns 1 s of 6-DOF IMU data into forward velocity, like a wheel sensor.
B. Auto-Calibration : Low-pass gravity + PCA aligns any phone mount to the vehicle axes.
C. ESKF Fusion : Learns phone IMU bias under open sky; switches to AI speed in <10 ms on blackout.
D. HMM Map-Matching : Viterbi on offline OSM snaps drifted paths back onto the road.
UVP (UNIQUE VALUE PROPOSITION)
AI-Triggered ZUPT : Detects idling vibration and freezes drift in traffic.
NHC + Vibe-Based Covariance : Blocks sideways/vertical motion; adapts trust to road roughness.
Zero-Latency C++ (Eigen via JNI) : No garbage-collection pauses, low battery drain.

## Slide 3: TECHNICAL APPROACH
@Enigm
@
3
@SIH Idea submission- Template
@Enigm
@
1 Ingestion & Auto-Calibration
6-DOF IMU read at 100 Hz
Low-pass filter finds gravity (Z)
PCA finds forward vector (X)
3D rotation aligns phone to car
2 Parallel AI + Physics Split
Path A :
NHC forces Vy = Vz = 0
Path B : TFLite 1D-CNN predicts Vx, filters potholes
ZUPT : idle-engine classifier forces V = 0
3 GNSS + INS Fusion (ESKF)
GNSS on :
learn zero-g bias
GNSS off :
switch in <10 ms
AI velocity + NHC − stored bias = dead reckoning
4 Map-Matching Layer
Overlay X,Y on offline OSM grid
HMM + Viterbi checks road topology
Snaps drifted path to nearest lane
5 Output (UI Layer)
Corrected coordinates to Kotlin UI
Seamless 10 Hz navigation
No map freeze or jump
TECH STACK
Model Training
Python · PyTorch · Pandas · SciPy (FFT)
On-Device AI
TFLite / ONNX · INT8 quantized · NNAPI (NPU)
Mobile Engine
Kotlin · C++ + Eigen via JNI · Mapbox / Google Maps SDK
Map & Routing
Valhalla · OpenStreetMap · HMM
Enterprise Edge
ROS2 (C++) · 200 Hz FOG IMU

## Slide 4: FEASIBILITY AND VIABILITY
@Enigm
@
4
@SIH Idea submission- Template
@Enigm
@
FEASIBILITY
Technical : ESKF and NHC are proven in robotics & luxury cars; C++/JNI handles 100 Hz IMU without GC pauses.
Data : IO-VNBD pairs phone IMU with CAN odometry ground truth to train the 1D-CNN with no extra hardware.
Operational : 100% software: no OBD-II dongle, no mechanic, just an app install.
VIABILITY
Economic : Runs on existing budget Android phones, so deployment cost is near zero.
Market : Fits Zomato, Swiggy, Delhivery & Uber gig fleets losing time and fuel to lost GNSS.
Scalability : Hardware-agnostic bias learning works on any phone brand; ROS2 mode extends it to fleets.
CHALLENGES & MITIGATION
Battery & Heat
Challenge : Continuous 100 Hz deep learning can overheat budget phones and cause throttling.
Mitigation : INT8 quantization (4x smaller) + NNAPI delegation to NPU/DSP instead of CPU.
Phone Placement
Challenge : Phone may sit upside down, on a vibrating handle, or be knocked sideways.
Mitigation : Continuous LPF + PCA re-alignment recomputes the rotation matrix with no user input.
Sensor Fragmentation
Challenge : Bosch, TDK & ST IMUs have different noise profiles; a fixed algorithm fails.
Mitigation : ESKF learns each phone's zero-g bias from GNSS and subtracts it during blackout.

## Slide 5: IMPACT AND BENEFITS
@Enigm
@
5
@SIH Idea submission- Template
@Enigm
@
IMPACT ON TARGET AUDIENCE & ECOSYSTEM
Economic & Logistics : Gig drivers lose time and fuel to missed exits in underpasses and parking lots. Lane-level tracking avoids re-routing and improves ETAs.
Safety : No more frozen or jumping maps after a signal loss, so less sudden braking, illegal U-turns and distraction.
Social & Digital Scale : Brings luxury-car dead reckoning to 2-wheelers, autos and older trucks at zero hardware cost.
Feature | Google Maps | Hardware INS | NaviCore AI
Tracks in tunnels | No (freezes) | Yes | Yes, seamless
Hardware needed | Smartphone | OBD-II / wheel sensors | Smartphone
AI pothole/noise filter | No | No | Yes (1D-CNN)
Drift freeze in traffic | No | No | Yes (ZUPT)
Any mounting angle | N/A | No, fixed | Yes (PCA)
Cost | Free | ₹20,000 – ₹1,00,000+ | Free, software only
HOW NAVICORE WORKS
MODE 1: OPEN-SKY FUSION
Scenario : Clear sky, strong GNSS
Action : AI sleeps to save NPU power; ESKF learns the phone's zero-g bias
Output : Accurate position at 10 Hz
MODE 2: AI DEAD RECKONING
Scenario : Tunnel, basement or dense forest
Action : Switch in <10 ms; 1D-CNN speed + ZUPT for traffic jams
Output : Drift below 10% (<5 m over 50 m)
MODE 3: ENTERPRISE EDGE
Scenario : Autonomous / military logistics
Action : C++ core on ROS2 with 200 Hz FOG IMU
Output : Modular engine beyond smartphones

## Slide 6: RESEARCH AND REFERENCES
@Enigm
@
AI-IMU Dead-Reckoning : Brossard et al. (IEEE T-RO): AI predicts sensor noise better than full trajectories, the basis for decoupling AI from the physics engine.
RoNIN : Robust neural inertial navigation: 1D-CNNs on continuous 6-DOF IMU time series.
NHC Kinematics : Standard non-holonomic constraint model for four-wheeled ground vehicles.
IO-VNBD Dataset : Time-synced smartphone IMU (input) + vehicle CAN-bus odometry (ground truth), so no RTK-GPS collection needed.
Google Maps / MapmyIndia : Basic extrapolation fails in jams and curved tunnels; cannot filter phone vibration.
Hardware INS : Accurate but costs thousands of dollars, needs OBD-II, and cannot fit two-wheelers.
100% Software : Luxury-grade accuracy on budget phones.
AI Noise Filtering : Separates real motion from potholes and idling.
Zero-Latency + Self-Calibrating : Native C++ Kalman filter; any mounting angle.
EDA on IO-VNBD :
System Architecture :
Demo Video :
Existing solutions
Our Solution
PROJECT RESOURCES
@Enigm
@